## Slide 1
Start
k = 0
Channel has been continuously free over DIFS?
No
ACK is received?
Transmit the frame
Wait until the channel becomes free
Wait until channel is continuously free over DIFS
W = min{2k (Wmin+1) - 1,Wmax}
BIslots = rand[0,W]
w = BIslots
No
Yes
Channel is continuously free over IFS?
No
Channel is continuously free over ST?
w = w - 1
w = 0 ?
Yes
Yes
ACK is timed out?
Wait for new frame
k = k + 1
k > Kmax?
Kmax: the maximum number of frame re-transmissions
Drop the frame
No
Yes
No
Yes
Exponential
back-off
procedure
Yes
Yes
Wait until an ACK event