## Slide 1: Mahsa Derakhshani mahsa.derakhshani@mail.mcgill.ca
Overview of Ad Hoc Networks and Wi-Fi
Lectures 22-23

## Slide 2: Lectures 22-23 - Outline
Introduction of Ad Hoc Networks
Applications of Ad Hoc Networks
Technical Challenges
Design Principles
  MAC Protocols
  Routing Protocols
Overview of 802.11 Standards
  PHY Evolution
  MAC Evolution
  State of the Art: 802.11ac and 802.11ad

## Slide 3: Introduction on Ad Hoc Wireless Networks
Peer-to-peer communications: No backbone infrastructure
Self-organizing network
Multi-hop routing: Each station plays the role of router
Dynamic topology

## Slide 4: Ad Hoc vs. Cellular Wireless Networks
Cellular Networks | Ad-hoc Networks
Fixed, pre-located cell sites and base stations | No fixed base stations, very rapid deployment
Static backbone network topology | Highly dynamic network topologies
Relatively favorable environment and stable connectivity | Hostile environment (losses, noise) and irregular connectivity
Detailed planning before base stations can be installed | Ad hoc network automatically forms and conforms to change
High setup costs and large setup time | Cost-effective and less setup time

## Slide 5: Applications for Ad Hoc Networks
Applications | Descriptions/Services
Data Networks | Support direct data exchange between personal digital assistants (PDAs) without having an access point
Sensor Networks | Collection of a large number of small nodes with sensing, computation, and wireless networking capabilities, used to collect real time data to automate everyday functions. There is a wide range of applications for sensor networks, e.g., healthcare monitoring, industrial monitoring, smart grid and etc.
Tactical Networks | Military communications at battlefield where there is no network infrastructure

## Slide 6: Technical Challenges of Ad Hoc Networks
Limited transmission range
Scalability
Energy constraints
Routes changes
Packet losses
Device heterogeneity

## Slide 7: Technical Challenges of Ad Hoc Networks
Hidden terminals
Exposed terminals

## Slide 8: Designs Principles of Ad Hoc Networks
Physical layer design
Data Link layer (MAC) design
Network layer design
  Neighbor discovery and topology control
  Routing
  Resource allocation and flow control
Transport layer design
Application layer design
Cross layer design

## Slide 9: Medium Access Control Protocols
Medium Access Control (MAC) protocol
  How users share spectrum and ensure successful packet transmission
Required features and challenges
  Distributed operation
  Capability of power control
  Responsible for retransmissions
  Fairness: especially for relaying nodes
  Real-time traffic support
  Access delay

## Slide 10: Medium Access Control Protocols
MAC Protocols for Ad Hoc
Wireless Networks
Contention-based Protocols
with Scheduling Mechanisms
Contention-based Protocols
with Reservation Mechanisms
Synchronous
Protocols
Asynchronous
Protocols
Contention-based Protocols
Sender-initiated
Protocols
Receiver-initiated
Protocols
Single-channel
Protocols
Multi-channel
Protocols

## Slide 11: Medium Access Control Protocols
Sender-initiated MAC protocol
Receiver-initiated MAC protocol

## Slide 12: Power Control
Power control across all nodes in the network is part of MAC layer design
The main role is to ensure SINR targets for all links
It is often impossible to meet the SINR constraints
  Large number of interferers
  Range of channels gains associated with all signals in the network
A distributed iterative power control algorithm
  Fixed channel gains are considered
  The transmitter link updates its transmit power at time

## Slide 13: Automatic Repeat Request (ARQ)
  Access layer is responsible for retransmission of packets received in errors.
  Receiver informs the transmitter about corrupted packet (NACK).
  Standard ARQ: retransmitting the original packet
  ARQ with incremental redundancy: transmitting some additional coded bits to provide a stronger error correction capability

## Slide 14: Routing Protocols
Routing Protocols for Ad Hoc
Wireless Networks
Reactive / On-demand
Flooding
Centralized
Proactive / Table-driven
Source-driven
Distributed
The routing protocol in an ad hoc wireless network is a significant design challenge
  No distinction between routers and nodes
  No external network setup: “Self-configuring”
  Node mobility

## Slide 15: Routing Protocols-Flooding

## Slide 16: Routing – Flooding Protocol
Advantages
  Simplicity
  Robust to changing network topology
  Requires little routing overhead
Disadvantages
  Multiple copies of the same packet traverse through the network
  Wasting bandwidth
  Wasting battery power

## Slide 17: Routing – Proactive Protocols
Proactive protocols
  Determine routes independent of traffic pattern
  Collect information about channel conditions and network topology
  Compute routing tables for all the nodes in the network
  Update routing tables at regular intervals because of network dynamics
Route optimization criteria
  Distance vector routing minimize hop counts
  Link state routing minimize a cost function associated with each link such as delay

## Slide 18: Routing – Reactive Protocols
Reactive protocols
  Discover routes and maintain them only at the initiation of a source node that has traffic to send to a given destination
  Eliminate the overhead of maintaining routing tables for routes not currently in use (advantage)
  Entail significant initial delay because route discovery process is just initiated when there is data to send (disadvantage)
Hybrid protocols
  Reactive and proactive routing are combined
  Reduce the delay associated with reactive routing
  Reduce the overhead associated with proactive routing

## Slide 19: Routing – Hybrid Protocols
Zone routing protocol
  If a packet's destination is in the same zone as the sender, the proactive protocol using an already stored routing table is used to deliver the packet immediately.
  If the route extends outside the packet's originating zone, a reactive protocol takes over to check each successive zone in the route to see whether the destination is inside that zone.

## Slide 20: Routing – Hybrid Protocols
Zone routing protocol

## Slide 21: Flow Control
A routing protocol dictates the route a packet follow from a source node to its destination.
If routing sends two much data over a given link congestion
Routing protocol flow control
The delay associated with a given link
Routing, resource allocation and flow control are all interdependent.

## Slide 22: Network Capacity Limits
For a network of nodes => links
Scaling law
  Throughput per node decreases with , at a rate between and
  Throughput per node goes to zero, when
  Total network throughput increase with , at a rate between and
  The reason is that intermediate nodes spend much of their resources forwarding for others
  It is a pessimistic result: it assumes that nodes choose their destination node at random.

## Slide 23: Network Capacity Limits
Capacity region slice of a five-node network
  Nodes are randomly located in a square area
  Channel model: Path-loss
  R12: Achievable rate from node 1to 2
  R34: Achievable rate from node 3 to 4
  Other nodes just relaying
  Variable rate transmission
  (a) single-hop, (b) multihop, (c) multihop with spatial reuse, (d) power control and (e) successive interference cancellation.

## Slide 24: Wireless Sensor Networks
Nodes powered by non-rechargeable batteries
Data flows to centralized location
Low per-node rates but up to 100,000 nodes.
Data highly correlated in time and space.
Nodes can cooperate in transmission, reception, compression, and signal processing.

## Slide 25: Wireless Protocols Comparison

## Slide 26: IEEE 802.15.4 / ZigBee Radios
IEEE 802.15.4 is a set of MAC and PHY specifications for implementing low-rate wireless personal area network (LR-WPAN)
Low-cost, low-rate and short-range communications between devices
Network Topology: Star clusters or peer-to-peer operation
PAN
Coordinator

## Slide 27: IEEE 802.15.4 / ZigBee Radios
PHY
  Frequency of operation in ISM bands, data rates of 20, 40 and 250 kbps
  Direct sequence spread spectrum, BPSK, ASK and O-QPSK
MAC
  Hybrid CSMA/CA and TDMA channel access
  Beacon management, guaranteed time slot management, association and disassociation, acknowledged frame delivery
868.3 MHz
Channel 0
Channels 1-10
928 MHz
902 MHz
2 MHz
2.4 GHz
Channels 11-26
2.4835 GHz
5 MHz

## Slide 28: IEEE Standards - Wi-Fi
IEEE 802.11 is a set of MAC and PHY specifications for implementing wireless local area network (WLAN)
IEEE 802.11 standard defines two operation modes: ad hoc mode and infrastructure mode
  In ad hoc mode, users communicate directly with each other without the use of a wireless access point (AP) Independent Basic Service Set (IBSS)
  In infrastructure mode, users communicate with each other through a wireless AP Basic Service Set (BSS)

## Slide 29: IEEE Standards - Wi-Fi
Wi-Fi is becoming ubiquitous
Number of public hotspots worldwide

## Slide 30: Evolution of Wi-Fi

## Slide 31: 802.11 Standards: PHY Evolution

## Slide 32: 802.11 Standards: PHY Evolution

## Slide 33: 802.11 Standards: MAC Evolution

## Slide 34: Original 802.11 MAC
Point Coordination Function (PCF)
  Polled access through AP and distributed access
  Contention-free period (CFP) and contention period (CP)
  Seldom implemented in practice
Distributed Coordination Function (DCF)
  Two-way handshaking: Carrier sense multiple access (CSMA) with immediate ACK
  Four-way handshaking : RTS/CTS exchange (optional)

## Slide 35: Original 802.11 MAC
Two-way handshaking CSMA-based MAC mechanism
Distributed inter-frame space (DIFS)
  Each user has to sense the channel idle for a DIFS prior to transmission
The discrete-time binary exponential backoff mechanism
  The backoff time is selected according to a uniform distribution in the interval (0,CW)
Once the data packet is received successfully
  The receiver waits for a period of time called short inter-frame space (SIFS)
  Then , it sends an acknowledgement (ACK)

## Slide 36: Original 802.11 MAC
Four-way handshaking RTS/CTS access mechanism
  Improves throughput performance
  Resolves hidden terminal problem
RTS
Contention
Contention
USER2
SIFS
USER1
DATA
ACK
DIFS
RTS
CTS
DATA
ACK
5 4
2 1
6 5 4
3 2 1
DIFS

## Slide 37: 802.11 MAC Enhancements
802.11e enhances DCF and PCF through Hybrid Coordination Function (HCF), to support multimedia applications with QoS
HCF controlled channel access (HCCA)
  Improved variant of PCF requiring a central coordinator that schedules medium access.
  No device implementing HCCA is known to exist in the market.
Enhanced Distributed Channel Access (EDCA)
  An extension to the legacy CSMA-based DCF mechanism
  Supports four traffic categories: video, voice, best effort, background
  Enables service differentiation
  EDCA variant called Wi-Fi multimedia (WMM)

## Slide 38: Enhanced Distributed Channel Access (EDCA)
Applications assign each data packet to an AC
Packets are added to one of four independent transmit queues
Different inter frame spaces and contention windows for ACs
Data packets with higher priorities get higher chance of access

## Slide 39: Enhanced Distributed Channel Access (EDCA)
Internal contention

## Slide 40: Enhanced Distributed Channel Access (EDCA)
Backoff mechanism

## Slide 41: EDCA – Transmission Opportunity (TXOP)
In addition to the differentiation & prioritization, 802.11e introduces TXOP.
A TXOP is a bounded time interval during which a station can send as many frames as possible (as long as the duration of the transmissions does not extend beyond the maximum duration of the TXOP).
  A station cannot transmit a frame that extents beyond a TXOP. If a frame is too large, it should be fragmented to smaller ones
Advantages
  Reduces the problem of low rate stations gaining an inordinate amount of channel time
  Reduces network overhead (due to backoff for each single frame transmission)

## Slide 42: 802.11 MAC Enhancements
Frame Aggregation
  Required procedure that each single packet traverses from the time it arrives at the MAC until it is successfully received by the receiver
  To improve throughput reduce frequency of PHY and MAC headers

## Slide 43: 802.11 MAC Enhancements
Frame Aggregation
  To reduce overhead and waiting time, one solution is concatenating or packing multiple packets together and adding the overheads over the group rather separate ones

## Slide 44: 802.11 MAC Enhancements
Block Acknowledgment
All the frames sent (during a TXOP period) are acknowledged by a unique Block Acknowledgement (BA) instead of an ACK frame for each frame transmitted
The station transmits a request for BA (BAR), and the receiver respond with BA after a SIFS period
Missing frames are retransmitted
Can significantly reduce management overhead

## Slide 45: 802.11 MAC Enhancements
TXOP Sharing or MU-TXOP
Enables multiple downlink traffic streams to multiple receiver stations simultaneously

## Slide 46: 802.11 MAC Enhancements
TXOP Sharing or MU-TXOP

## Slide 47: 802.11 MAC Enhancements
All expected MAC enhancement

## Slide 48: State of the Art: IEEE 802.11ac
Operates in the 5GHz band
Key features that enable data rates up to 6.9Gbps
  Up to 8 antennas and spatial streams
  Wider channel BW (20/40/80/160MHz)
  Downlink multi-user MIMO
  256 QAM
First generation ac chips are already available in the market
Usage cases cover both enterprise and home
Focus is on link throughput, rather than efficient use of spectrum resources
11ac is backward compatible with 11a and 11n

## Slide 49: IEEE 802.11ac Usage Models
Wireless Display | Desktop Storage & Display
 | Projection to TV or projector in conf room (lightly compressed video)
 | In room gaming (lightly compressed video)
 | Streaming from camcorder to display (lightly compressed video)
 | Broadcast TV field pick up
Distribution of HDTV | Lightly compressed video streaming around the home
 | Compressed video streaming around home
 | Intra large vehicle (e.g. airplane) applications
 | Wireless networking for office
 | Remote medical assistance
Rapid upload/download | Rapid sync-n-go file transfer
 | Picture by picture viewing
 | Airplane docking
 | Movie content download to car
 | Police / surveillance car upload
Backhaul | Multi-media mesh backhaul
 | Point-to-point backhaul
Outdoor campus / auditorium | Video demos / tele-presence in auditorium
 | Public safety mesh
Manufacturing floor | Manufacturing floor automation

## Slide 50: IEEE 802.11ac Usage Model Example
Delivering multiple HD video streams simultaneously
802.11ac usage model example: In-home HD content distribution

## Slide 51: 802.11ac Usage Model Example
802.11ac in 40 MHz with eight antenna AP can supports two HD video streams at 24 Mbps each and two Blu-Ray video streams at 54 Mbps each

## Slide 52: IEEE 802.11ac Features
Mandatory 5 GHz operation
  Less interference and more non-overlapping channels
Wider bandwidth
  It introduces 80MHz and 160MHz in addition to 20MHz and 40MHz.

## Slide 53: IEEE 802.11ac Features
Higher order modulation
  256 QAM instead of 64 QAM in 802.11n
Higher order MIMO
  Maximum number of spatial streams is increased to eight

## Slide 54: IEEE 802.11ac Features
Multi-user MIMO
  First Wi-Fi standard introduces MIMO, to serve up to four clients simultaneously.
Standard-based beamforming
  802.11ac defines a single explicit compressed feedback for beamforming
Backwards compatibility to 802.11a/n
  802.11ac enables coexistence by a backwards compatible preamble which understandable by 802.11 a/n

## Slide 55: IEEE 802.11ac Features
Improved interference detection threshold
Enhanced RTS/CTS with bandwidth indication
  Enables dynamic bandwidth management and optimizing the use of wider bandwidth in an efficient manner
  Each Network has a 20 MHz primary channel for carrier sensing
  Once the access to the primary channel is obtained, additional secondary channels for wider bandwidth may be added.

## Slide 56: Coverage

## Slide 57: Coverage
Single Family Units =>Range is short enough
Possible solutions for Multi Dwelling Units
  1- Radio resource management
  2- Primary channel assignment
  3- Beamforming

## Slide 58: State of the Art: IEEE 802.11ad
60 GHz operation Throughput intensive applications
2.16GHz channel bandwidth
Short range Personal Area Network (PAN)
Personal Basic Service Set (PBSS)

## Slide 59: State of the Art: IEEE 802.11ad
Beamforming would be the key technology to enhance 60GHz range.
Beamforming utilizes multiple antenna elements to form a beam toward a certain direction with increased signal strength
However, beamforming could only be functional after discovery and training of the target device.

## Slide 60: State of the Art: IEEE 802.11ad
60GHz Training Frame could be configured in a way that it contains multiple beam patterns
  60GHz Training Frame could be signalled with 2.4/5GHz frame
The beamformee could report back the strongest beam pattern it receives
  Feedback can be sent using 2.4/5GHz training frames

## Slide 61: State of the Art: IEEE 802.11ad
MAC Design
  Needs to support high throughput, directional communications and QoS improvement
Scheduling scheme, wherein a station is allowed to access the channel without a central controller involvement is preferable; this is facilitated by having the central controller distribute the channel time schedule
  Good framework for QoS, power management
  Spatial reuse
    Good for BSS as physically distributed stations can be scheduled simultaneously
  Lends itself well to directional communication since stations know who they will talk to and hence can steer their antenna to the right direction,

## Slide 62: State of the Art: IEEE 802.11ad
Beacon frame format:
BT/Directional Association: AP broadcasts beacons in different direction
A-BFT/Beamforming: Beamforming processing
AT: Announcement Time: Management request-response frame ex-changes between AP and station
CBP: Access during CBP is based on a modified 802.11e EDCA access mechanism that is fine tuned or directional communication
SP: TDMA access mechanism Access: during